## Slide 1
Introduction to Assembly Language

## Slide 2: Presentation Outline
Basic Elements of Assembly Language
Flat Memory Program Template
Example: Adding and Subtracting Integers
Assembling, Linking, and Debugging Programs
Defining Data
Defining Symbolic Constants
Data-Related Operators and Directives

## Slide 3: Constants
Integer Constants
  Examples: –10, 42d, 10001101b, 0FF3Ah, 777o
  Radix: b = binary, d = decimal, h = hexadecimal, and o = octal
  If no radix is given, the integer constant is decimal
  A hexadecimal beginning with a letter must have a leading 0
Character and String Constants
  Enclose character or string in single or double quotes
  Examples: 'A', "d", 'ABC', "ABC", '4096'
  Embedded quotes: "single quote ' inside", 'double quote " inside'
  Each ASCII character occupies a single byte

## Slide 4: Assembly Language Statements
Three types of statements in assembly language
  Typically, one statement should appear on a line
Executable Instructions
  Generate machine code for the processor to execute at runtime
  Instructions tell the processor what to do
Assembler Directives
  Provide information to the assembler while translating a program
  Used to define data, select memory model, etc.
  Non-executable: directives are not part of instruction set
Macros
  Shorthand notation for a group of statements
  Sequence of instructions, directives, or other macros

## Slide 5: Instructions
Assembly language instructions have the format:
[label:] mnemonic [operands] [;comment]
Instruction Label (optional)
  Marks the address of an instruction, must have a colon :
  Used to transfer program execution to a labeled instruction
Mnemonic
  Identifies the operation (e.g. MOV, ADD, SUB, JMP, CALL)
Operands
  Specify the data required by the operation
  Executable instructions can have zero to three operands
  Operands can be registers, memory variables, or constants

## Slide 6: Instruction Examples
No operands
  stc ; set carry flag
One operand
  inc eax ; increment register eax
  call Clrscr ; call procedure Clrscr
  jmp L1 ; jump to instruction with label L1
Two operands
  add ebx, ecx ; register ebx = ebx + ecx
  sub var1, 25 ; memory variable var1 = var1 - 25
Three operands
  imul eax,ebx,5 ; register eax = ebx * 5

## Slide 7: Comments
Comments are very important!
  Explain the program's purpose
  When it was written, revised, and by whom
  Explain data used in the program
  Explain instruction sequences and algorithms used
  Application-specific explanations
Single-line comments
  Begin with a semicolon ; and terminate at end of line
Multi-line comments
  Begin with COMMENT directive and a chosen character
  End with the same chosen character

## Slide 8: Next . . .
Basic Elements of Assembly Language
Flat Memory Program Template
Example: Adding and Subtracting Integers
Assembling, Linking, and Debugging Programs
Defining Data
Defining Symbolic Constants
Data-Related Operators and Directives

## Slide 9: Flat Memory Program Template
TITLE Flat Memory Program Template (Template.asm)
; Program Description:
; Author: Creation Date:
; Modified by: Modification Date:
.686
.MODEL FLAT, STDCALL
.STACK
INCLUDE Irvine32.inc
.DATA
; (insert variables here)
.CODE
main PROC
; (insert executable instructions here)
exit
main ENDP
; (insert additional procedures here)
END main

## Slide 10: TITLE and .MODEL Directives
TITLE line (optional)
  Contains a brief heading of the program and the disk file name
.MODEL directive
  Specifies the memory configuration
  For our purposes, the FLAT memory model will be used
    Linear 32-bit address space (no segmentation)
  STDCALL directive tells the assembler to use …
    Standard conventions for names and procedure calls
.686 processor directive
  Used before the .MODEL directive
  Program can use instructions of Pentium P6 architecture
  At least the .386 directive should be used with the FLAT model

## Slide 11: .STACK, .DATA, & .CODE Directives
.STACK directive
  Tells the assembler to define a runtime stack for the program
  The size of the stack can be optionally specified by this directive
  The runtime stack is required for procedure calls
.DATA directive
  Defines an area in memory for the program data
  The program's variables should be defined under this directive
  Assembler will allocate and initialize the storage of variables
.CODE directive
  Defines the code section of a program containing instructions
  Assembler will place the instructions in the code area in memory

## Slide 12: INCLUDE, PROC, ENDP, and END
INCLUDE directive
  Causes the assembler to include code from another file
  We will include Irvine32.inc provided by the author Kip Irvine
    Declares procedures implemented in the Irvine32.lib library
    To use this library, you should link Irvine32.lib to your programs
PROC and ENDP directives
  Used to define procedures
  As a convention, we will define main as the first procedure
  Additional procedures can be defined after main
END directive
  Marks the end of a program
  Identifies the name (main) of the program’s startup procedure

## Slide 13: Next . . .
Basic Elements of Assembly Language
Flat Memory Program Template
Example: Adding and Subtracting Integers
Assembling, Linking, and Debugging Programs
Defining Data
Defining Symbolic Constants
Data-Related Operators and Directives

## Slide 14: Adding and Subtracting Integers
TITLE Add and Subtract (AddSub.asm)
; This program adds and subtracts 32-bit integers.
.686
.MODEL FLAT, STDCALL
.STACK
INCLUDE Irvine32.inc
.CODE
main PROC
mov eax,10000h ; EAX = 10000h
add eax,40000h ; EAX = 50000h
sub eax,20000h ; EAX = 30000h
call DumpRegs ; display registers
exit
main ENDP
END main

## Slide 15: Example of Console Output
Procedure DumpRegs is defined in Irvine32.lib library
It produces the following console output,
showing registers and flags:
EAX=00030000 EBX=7FFDF000 ECX=00000101 EDX=FFFFFFFF
ESI=00000000 EDI=00000000 EBP=0012FFF0 ESP=0012FFC4
EIP=00401024 EFL=00000206 CF=0 SF=0 ZF=0 OF=0

## Slide 16: Suggested Coding Standards
Some approaches to capitalization
  Capitalize nothing
  Capitalize everything
  Capitalize all reserved words, mnemonics and register names
  Capitalize only directives and operators
  MASM is NOT case sensitive: does not matter what case is used
Other suggestions
  Use meaningful identifier names
  Use blank lines between procedures
  Use indentation and spacing to align instructions and comments
    Use tabs to indent instructions, but do not indent labels
    Align the comments that appear after the instructions

## Slide 17: Understanding Program Termination
The exit at the end of main procedure is a macro
  Defined in Irvine32.inc
  Expanded into a call to ExitProcess that terminates the program
  ExitProcess function is defined in the kernel32 library
  We can replace exit with the following:
  push 0 ; push parameter 0 on stack
  call ExitProcess ; to terminate program
  You can also replace exit with: INVOKE ExitProcess, 0
PROTO directive (Prototypes)
  Declares a procedure used by a program and defined elsewhere
  ExitProcess PROTO, ExitCode:DWORD
  Specifies the parameters and types of a given procedure

## Slide 18: Modified Program
TITLE Add and Subtract (AddSubAlt.asm)
; This program adds and subtracts 32-bit integers
.686
.MODEL flat,stdcall
.STACK 4096
; No need to include Irvine32.inc
ExitProcess PROTO, dwExitCode:DWORD
.code
main PROC
mov eax,10000h ; EAX = 10000h
add eax,40000h ; EAX = 50000h
sub eax,20000h ; EAX = 30000h
push 0
call ExitProcess ; to terminate program
main ENDP
END main

## Slide 19: Next . . .
Basic Elements of Assembly Language
Flat Memory Program Template
Example: Adding and Subtracting Integers
Assembling, Linking, and Debugging Programs
Defining Data
Defining Symbolic Constants
Data-Related Operators and Directives

## Slide 20: Assemble-Link-Debug Cycle
Editor
  Write new (.asm) programs
  Make changes to existing ones
Assembler: ML.exe program
  Translate (.asm) file into object (.obj) file in machine language
  Can produce a listing (.lst) file that shows the work of assembler
Linker: LINK32.exe program
  Combine object (.obj) files with link library (.lib) files
  Produce executable (.exe) file
  Can produce optional (.map) file
Edit
Assemble
Link
Run
prog.asm
prog.obj
prog.lst
prog.exe
prog.map
library.lib
Debug

## Slide 21: Assemble-Link-Debug Cycle – cont'd
MAKE32.bat
  Batch command file
  Assemble and link in one step
Debugger: WINDBG.exe
  Trace program execution
    Either step-by-step, or
    Use breakpoints
  View
    Source (.asm) code
    Registers
    Memory by name & by address
    Modify register & memory content
  Discover errors and go back to the editor to fix the program bugs
Edit
Assemble
Link
Run
prog.asm
prog.obj
prog.lst
prog.exe
prog.map
library.lib
Debug

## Slide 22: Listing File
Use it to see how your program is assembled
Contains
  Source code
  Object code
  Relative addresses
  Segment names
  Symbols
    Variables
    Procedures
    Constants
Object & source code in a listing file
00000000 .code
00000000 main PROC
00000000 B8 00060000 mov eax, 60000h
00000005 05 00080000 add eax, 80000h
0000000A 2D 00020000 sub eax, 20000h
0000000F 6A 00 push 0
00000011 E8 00000000 E call ExitProcess
00000016 main ENDP
END main
object code
(hexadecimal)
source code
Relative
Addresses

## Slide 23: Next . . .
Basic Elements of Assembly Language
Flat Memory Program Template
Example: Adding and Subtracting Integers
Assembling, Linking, and Debugging Programs
Defining Data
Defining Symbolic Constants
Data-Related Operators and Directives

## Slide 24: Intrinsic Data Types
BYTE, SBYTE
  8-bit unsigned integer
  8-bit signed integer
WORD, SWORD
  16-bit unsigned integer
  16-bit signed integer
DWORD, SDWORD
  32-bit unsigned integer
  32-bit signed integer
QWORD, TBYTE
  64-bit integer
  80-bit integer
REAL4
  IEEE single-precision float
  Occupies 4 bytes
REAL8
  IEEE double-precision
  Occupies 8 bytes
REAL10
  IEEE extended-precision
  Occupies 10 bytes

## Slide 25: Data Definition Statement
Sets aside storage in memory for a variable
May optionally assign a name (label) to the data
Syntax:
[name] directive initializer [, initializer] . . .
  val1 BYTE 10
All initializers become binary data in memory

## Slide 26: Defining BYTE and SBYTE Data
value1 BYTE 'A' ; character constant
value2 BYTE 0 ; smallest unsigned byte
value3 BYTE 255 ; largest unsigned byte
value4 SBYTE -128 ; smallest signed byte
value5 SBYTE +127 ; largest signed byte
value6 BYTE ? ; uninitialized byte
Each of the following defines a single byte of storage:
MASM does not prevent you from initializing a BYTE with a negative value, but it's considered poor style.
If you declare a SBYTE variable, the Microsoft debugger will automatically display its value in decimal with a leading sign.

## Slide 27: Defining Byte Arrays
list1 BYTE 10,20,30,40
list2 BYTE 10,20,30,40
BYTE 50,60,70,80
BYTE 81,82,83,84
list3 BYTE ?,32,41h,00100010b
list4 BYTE 0Ah,20h,'A',22h
Examples that use multiple initializers

## Slide 28: Defining Strings
A string is implemented as an array of characters
  For convenience, it is usually enclosed in quotation marks
  It is often terminated with a NULL char (byte value = 0)
Examples:
str1 BYTE "Enter your name", 0
str2 BYTE 'Error: halting program', 0
str3 BYTE 'A','E','I','O','U'
greeting BYTE "Welcome to the Encryption "
BYTE "Demo Program", 0

## Slide 29: Defining Strings – cont'd
To continue a single string across multiple lines, end each line with a comma
menu BYTE "Checking Account",0dh,0ah,0dh,0ah,
"1. Create a new account",0dh,0ah,
"2. Open an existing account",0dh,0ah,
"3. Credit the account",0dh,0ah,
"4. Debit the account",0dh,0ah,
"5. Exit",0ah,0ah,
"Choice> ",0
End-of-line character sequence:
  0Dh = 13 = carriage return
  0Ah = 10 = line feed
Idea: Define all strings used by your program in the same area of the data segment

## Slide 30: Using the DUP Operator
Use DUP to allocate space for an array or string
  Advantage: more compact than using a list of initializers
Syntax
  counter DUP ( argument )
  Counter and argument must be constants expressions
The DUP operator may also be nested
var1 BYTE 20 DUP(0) ; 20 bytes, all equal to zero
var2 BYTE 20 DUP(?) ; 20 bytes, all uninitialized
var3 BYTE 4 DUP("STACK") ; 20 bytes: "STACKSTACKSTACKSTACK"
var4 BYTE 10,3 DUP(0),20 ; 5 bytes: 10, 0, 0, 0, 20
var5 BYTE 2 DUP(5 DUP('*'), 5 DUP('!')) ; '*****!!!!!*****!!!!!'

## Slide 31: Defining 16-bit and 32-bit Data
Define storage for 16-bit and 32-bit integers
  Signed and Unsigned
  Single or multiple initial values
word1 WORD 65535 ; largest unsigned 16-bit value
word2 SWORD –32768 ; smallest signed 16-bit value
word3 WORD "AB" ; two characters fit in a WORD
array1 WORD 1,2,3,4,5 ; array of 5 unsigned words
array2 SWORD 5 DUP(?) ; array of 5 signed words
dword1 DWORD 0ffffffffh ; largest unsigned 32-bit value
dword2 SDWORD –2147483648 ; smallest signed 32-bit value
array3 DWORD 20 DUP(?) ; 20 unsigned double words
array4 SDWORD –3,–2,–1,0,1 ; 5 signed double words

## Slide 32: QWORD, TBYTE, and REAL Data
quad1 QWORD 1234567812345678h
val1 TBYTE 1000000000123456789Ah
rVal1 REAL4 -2.1
rVal2 REAL8 3.2E-260
rVal3 REAL10 4.6E+4096
array REAL4 20 DUP(0.0)
QWORD and TBYTE
  Define storage for 64-bit and 80-bit integers
  Signed and Unsigned
REAL4, REAL8, and REAL10
  Defining storage for 32-bit, 64-bit, and 80-bit floating-point data

## Slide 33: Symbol Table
Assembler builds a symbol table
  So we can refer to the allocated storage space by name
  Assembler keeps track of each name and its offset
  Offset of a variable is relative to the address of the first variable
Example Symbol Table
.DATA Name Offset
value WORD 0 value 0
sum DWORD 0 sum 2
marks WORD 10 DUP (?) marks 6
msg BYTE 'The grade is:',0 msg 26
char1 BYTE ? char1 40

## Slide 34: Byte Ordering and Endianness
Processors can order bytes within a word in two ways
Little Endian Byte Ordering
  Memory address = Address of least significant byte
  Examples: Intel 80x86
Big Endian Byte Ordering
  Memory address = Address of most significant byte
  Examples: MIPS, Motorola 68k, SPARC
Byte 0
Byte 1
Byte 2
Byte 3
32-bit Register
MSB
LSB
. . .
. . .
Byte 0
Byte 1
Byte 2
Byte 3
a
a+3
a+2
a+1
Memory
address
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
32-bit Register
MSB
LSB
. . .
. . .
Byte 0
Byte 1
Byte 2
a
a+3
a+2
a+1
Memory
address

## Slide 35: Adding Variables to AddSub
TITLE Add and Subtract, Version 2 (AddSub2.asm)
.686
.MODEL FLAT, STDCALL
.STACK
INCLUDE Irvine32.inc
.DATA
val1 DWORD 10000h
val2 DWORD 40000h
val3 DWORD 20000h
result DWORD ?
.CODE
main PROC
mov eax,val1 ; start with 10000h
  add eax,val2 ; add 40000h
  sub eax,val3 ; subtract 20000h
  mov result,eax ; store the result (30000h)
  call DumpRegs ; display the registers
  exit
main ENDP
END main

## Slide 36: Next . . .
Basic Elements of Assembly Language
Flat Memory Program Template
Example: Adding and Subtracting Integers
Assembling, Linking, and Debugging Programs
Defining Data
Defining Symbolic Constants
Data-Related Operators and Directives

## Slide 37: Defining Symbolic Constants
Symbolic Constant
  Just a name used in the assembly language program
  Processed by the assembler  pure text substitution
  Assembler does NOT allocate memory for symbolic constants
Assembler provides three directives:
  = directive
  EQU directive
  TEXTEQU directive
Defining constants has two advantages:
  Improves program readability
  Helps in software maintenance: changes are done in one place

## Slide 38: Equal-Sign Directive
Name = Expression
  Name is called a symbolic constant
  Expression is an integer constant expression
Good programming style to use symbols
Name can be redefined in the program
COUNT = 500 ; NOT a variable (NO memory allocation)
. . .
mov eax, COUNT ; mov eax, 500
. . .
COUNT = 600 ; Processed by the assembler
. . .
mov ebx, COUNT ; mov ebx, 600

## Slide 39: EQU Directive
Three Formats:
Name EQU Expression Integer constant expression
Name EQU Symbol Existing symbol name
Name EQU <text> Any text may appear within < …>
No Redefinition: Name cannot be redefined with EQU
SIZE EQU 10*10 ; Integer constant expression
PI EQU <3.1416> ; Real symbolic constant
PressKey EQU <"Press any key to continue...",0>
.DATA
prompt BYTE PressKey

## Slide 40: TEXTEQU Directive
TEXTEQU creates a text macro. Three Formats:
Name TEXTEQU <text> assign any text to name
Name TEXTEQU textmacro assign existing text macro
Name TEXTEQU %constExpr constant integer expression
Name can be redefined at any time (unlike EQU)
ROWSIZE = 5
COUNT TEXTEQU %(ROWSIZE * 2) ; evaluates to 10
MOVAL TEXTEQU <mov al,COUNT>
ContMsg TEXTEQU <"Do you wish to continue (Y/N)?">
.DATA
prompt BYTE ContMsg
.CODE
MOVAL ; generates: mov al,10

## Slide 41: Next . . .
Basic Elements of Assembly Language
Flat Memory Program Template
Example: Adding and Subtracting Integers
Assembling, Linking, and Debugging Programs
Defining Data
Defining Symbolic Constants
Data-Related Operators and Directives

## Slide 42: OFFSET Operator
.DATA
bVal BYTE ? ; Assume bVal is at 00404000h
wVal WORD ?
dVal DWORD ?
dVal2 DWORD ?
.CODE
mov esi, OFFSET bVal ; ESI = 00404000h
mov esi, OFFSET wVal ; ESI = 00404001h
mov esi, OFFSET dVal ; ESI = 00404003h
mov esi, OFFSET dVal2 ; ESI = 00404007h
OFFSET = address of a variable within its segment
  In FLAT memory, one address space is used for code and data
  OFFSET = linear address of a variable (32-bit number)

## Slide 43: ALIGN Directive
ALIGN directive aligns a variable in memory
Syntax: ALIGN bound
  Where bound can be 1, 2, 4, or 16
Address of a variable should be a multiple of bound
Assembler inserts empty bytes to enforce alignment
.DATA ; Assume that
b1 BYTE ? ; Address of b1 = 00404000h
ALIGN 2 ; Skip one byte
w1 WORD ? ; Address of w1 = 00404002h
w2 WORD ? ; Address of w2 = 00404004h
ALIGN 4 ; Skip two bytes
d1 DWORD ? ; Address of d1 = 00404008h
d2 DWORD ? ; Address of d2 = 0040400Ch
w1
b1
404000
w2
404004
d1
404008
d2
40400C

## Slide 44: TYPE Operator
TYPE operator
  Size, in bytes, of a single element of a data declaration
.DATA
var1 BYTE ?
var2 WORD ?
var3 DWORD ?
var4 QWORD ?
.CODE
mov eax, TYPE var1 ; eax = 1
mov eax, TYPE var2 ; eax = 2
mov eax, TYPE var3 ; eax = 4
mov eax, TYPE var4 ; eax = 8

## Slide 45: LENGTHOF Operator
LENGTHOF operator
  Counts the number of elements in a single data declaration
.DATA
array1 WORD 30 DUP(?),0,0
array2 WORD 5 DUP(3 DUP(?))
array3 DWORD 1,2,3,4
digitStr BYTE "12345678",0
.code
mov ecx, LENGTHOF array1 ; ecx = 32
mov ecx, LENGTHOF array2 ; ecx = 15
mov ecx, LENGTHOF array3 ; ecx = 4
mov ecx, LENGTHOF digitStr ; ecx = 9

## Slide 46: SIZEOF Operator
.DATA
array1 WORD 30 DUP(?),0,0
array2 WORD 5 DUP(3 DUP(?))
array3 DWORD 1,2,3,4
digitStr BYTE "12345678",0
.CODE
mov ecx, SIZEOF array1 ; ecx = 64
mov ecx, SIZEOF array2 ; ecx = 30
mov ecx, SIZEOF array3 ; ecx = 16
mov ecx, SIZEOF digitStr ; ecx = 9
SIZEOF operator
  Counts the number of bytes in a data declaration
  Equivalent to multiplying LENGTHOF by TYPE

## Slide 47: Multiple Line Declarations
.DATA
array WORD 10,20,
30,40,
50,60
.CODE
mov eax, LENGTHOF array ; 6
mov ebx, SIZEOF array ; 12
A data declaration spans multiple lines if each line (except the last) ends with a comma
The LENGTHOF and SIZEOF operators include all lines belonging to the declaration
.DATA
array WORD 10,20
WORD 30,40
WORD 50,60
.CODE
mov eax, LENGTHOF array ; 2
mov ebx, SIZEOF array ; 4
In the following example, array identifies the first line WORD declaration only
Compare the values returned by LENGTHOF and SIZEOF here to those on the left

## Slide 48: PTR Operator
PTR Provides the flexibility to access part of a variable
Can also be used to combine elements of a smaller type
Syntax: Type PTR (Overrides default type of a variable)
.DATA
dval DWORD 12345678h
array BYTE 00h,10h,20h,30h
.CODE
mov al, dval
mov al, BYTE PTR dval
mov ax, dval
mov ax, WORD PTR dval
mov eax, array
mov eax, DWORD PTR array
78
56
34
12
dval
00
10
20
30
array
; error – why?
; al = 78h
; error – why?
; ax = 5678h
; error – why?
; eax = 30201000h

## Slide 49: LABEL Directive
Assigns an alternate name and type to a memory location
LABEL does not allocate any storage of its own
Removes the need for the PTR operator
Format: Name LABEL Type
.DATA
dval LABEL DWORD
wval LABEL WORD
blist BYTE 00h,10h,00h,20h
.CODE
mov eax, dval
mov cx, wval
mov dl, blist
wval
00
10
00
20
blist
dval
; eax = 20001000h
; cx = 1000h
; dl = 00h

## Slide 50: Summary
Instruction  executed at runtime
Directive  interpreted by the assembler
.STACK, .DATA, and .CODE
  Define the code, data, and stack sections of a program
Edit-Assemble-Link-Debug Cycle
Data Definition
  BYTE, WORD, DWORD, QWORD, etc.
  DUP operator
Symbolic Constant
  =, EQU, and TEXTEQU directives
Data-Related Operators
  OFFSET, ALIGN, TYPE, LENGTHOF, SIZEOF, PTR, and LABEL